## Slide 1
Elastic RSS
Alexander Rucker, Tushar Swamy, Muhammad Shahbaz, and Kunle Olukotun
Motivation
Current data plane software solutions are either too inflexible or slow
Design
Assign each packet to a scaling group
Estimate the per-packet workload
Determine core count for the scaling group
Select a virtual core
Estimate queue depths
Map the virtual core to a physical core
Evaluation
eRSS can be broken into the following steps:
Responsiveness
Co-Scheduling Packets and Cores using Programmable NICs
NIC
NIC
Sched
NIC
Elastic RSS (eRSS) is a system that extends traditional RSS by scheduling packets and cores using emerging programmable NICs with new abstractions like map-reduce
Low Latency Workload Scheduling
Elastic RSS (eRSS)
eRSS maps to a PISA NIC with map-reduce extensions
Map-reduce is supported with a coarse grain reconfigurable architecture
Software Manager
The software manager starts and pins a sleeping thread to each core
When the NIC allocates a core, it wakes up the resident thread
Cores can run any software, including distributed work stealing or preemption
Upon deallocation., the packet thread sleeps and the OS schedules a batch job
A software manager on the host CPU estimates request service times, allocates slack cores between scaling groups, and updates NIC shadow counters on a coarser timescale (e.g. 100 us)
In eRSS, processing is divided across two timescales: fine grained, per-packet processing at the NIC and coarse grained state management at the host CPU
Run: Server
Run: Batch
Sleep: Server
Run: Batch
Interrupt from NIC
NIC deallocates core
Poll NIC
Assign slack core
Linux Scheduler Tick
We evaluate three design points:
eRSS-a: aggressively provision cores so each is 90% busy
eRSS-c: conservatively provision cores so each is 75% busy
RSS: no core scheduling or weight adjustment
Tail Latency
Parameters control trade-off between core use and tail latency
eRSS runs at line rate using slight extensions to existing NICS
eRSS can be extended with ML for automatic operation
Parser
MAT
Scheduler
MAT
Map-Reduce
CDF
0.1
1
10
100
1
0.8
0.6
0.4
0.2
0
Latency (us)
eRSS-a
eRSS-c
RSS
Packet
RSS: 4 useful cores at 50% load
CPU-based Scheduling: 3 useful cores at 100%, incl. 1 for batch jobs
eRSS: 4 useful cores at 100%, incl. 2 for batch jobs
40
30
20
10
0
64
48
32
16
0
Cores Allocated
Req. Traffic (Gbps)
eRSS-a
eRSS-c
RSS
0
1
2
3
4
5
Time (ms)
Deepest Queue (kiB)
30
20
10
0