## Slide 1: Taurus: An Intelligent Data Plane
Alexander Rucker
Tushar Swamy, Muhammad Shahbaz, and Kunle Olukotun

## Slide 2: Managing networks is hard!
Cloud Computing
Internet of Things (IoT)
Augmented and Virtual
Reality (AR/VR)
Notes: - Many application domains
Cloud computing needs availability
AR/VR network needs to be low latency
IOT is very large scale
Not feasible for humans to manage, too many heuristic and ad-hoc solutions – we should use more data driven algorithms

## Slide 3: Approaches to manage networks are …
Data Plane
Switch or NIC
Fast yet dumb
Slow but intelligent
Control Plane
Intelligence
OR
Notes: Existing approaches can be divided into two categories:
  Slow and intel at Control Plane
  Fast but dumb at the Data Plane

## Slide 4: Approaches to manage networks are …
Data Plane
Switch or NIC
Fast yet dumb
Examples:
Congestion control
Load balancing (ECMP, RSS)
Queue scheduling
Characteristics:
Operates on packet scale
Low latency: ns
High throughput: Tbps
Uses heuristics: hash, …
Packets In
Packets Out
Notes: High perf constraints force us to use simple heuristics
Can’t do more complex operations at the data plane

## Slide 5: Approaches to manage networks are …
Data Plane
Switch or NIC
Fast yet dumb
Slow but intelligent
Control Plane
Intelligence
OR

## Slide 6: Approaches to manage networks are …
Data Plane
Switch or NIC
Slow but intelligent
Control Plane
Intelligence
Examples:
Anomaly detection
Automation
Recommendation
Characteristics:
Can do machine learning
Operates on flows
Millisecond latency
Low throughput
Packets In
Packets Out
Packet
Digest
Flow
Rule
Notes: - Distinction between packet and flow level
- Anomaly detection may miss packets at Control Plane
- Can do more complicated stuff but cant meet line rate and TP requirements

## Slide 7: Approaches to manage networks are …
Data Plane
Switch or NIC
Fast yet dumb
Slow but intelligent
Control Plane
Intelligence
OR

## Slide 8: Approaches to manage networks are …
Fast yet dumb
Slow but intelligent
Control Plane
Intelligence
Data Plane
Switch or NIC
OR

## Slide 9: Network management should be …
Fast and intelligent
Control Plane
Intelligence
Data Plane
Switch or NIC
Notes: We should have fast and intelligent systems that can operate at the packet granularity

## Slide 10: What does “Intelligence” mean?
Networks are becoming autonomous (Self Driving Networks)
Machine learning (ML) will play a key role in the future of networks [1,2,3]
Security
Control
Analytics
Notes: Start with ML Inference == Intelligence

## Slide 11: ML Inference: Neural Networks
Inputs
Outputs
Notes: - Let’s look at one of the more popular classes of ML algorithms
- What is a neural network?
- Weighted heuristic

## Slide 12: ML Inference: Neural Networks
Inputs
Outputs
Notes: Let’s focus on one neuron

## Slide 13: ML Inference: Single Neuron
x1
x0
x2
x3
Input
Features
W0
Neuron
Weights and Bias
*
+
B
+
G(z)
Activation
W1
W2
W3
*
*
*
+
+
Notes: Elem wise mult
Additions

## Slide 14: Can match-action tables perform ML inference?
Packet
Parser
Match-Action
Tables
Traffic
Manager
Packets In
Packets Out
Notes: - Why no MAT for ML:
Too many operations: Arithmetic intensity is too high
Not enough intermediate storage in PHV
Let’s revisit the neuron example and see what we would need to support

## Slide 15: ML Inference: Single Neuron
x1
x0
x2
x3
Input
Features
W0
Neuron
Weights and Bias
*
+
B
+
G(z)
Activation
W1
W2
W3
*
*
*
+
+
Map: Element-wise
multiplication
Reduce: Addition
using a tree
Notes: Mult looks like a map
Additions look like a reduction
We should support Map and Reduce parallel patterns

## Slide 16: Taurus: An Intelligent Data Plane
Packet
Parser
Match-Action
Tables
Map Reduce
Unit
Match-Action
Tables
Traffic
Manager
Packets In
Packets Out
Notes: Mention that this is VLIW + SIMD
We are NOT replacing MAT.
How do we build Map Reduce hardware

## Slide 17: Building blocks of Taurus: Map-Reduce
CU
MU
CU
MU
MU
CU
CU
MU
CU
Data In
Data In
Data Out
Data Out
Compute Units
Memory Units
Notes: - Reconfigurable grid of compute and memory units based on Plasticine architecture

## Slide 18: Building blocks of Taurus: Map-Reduce
CU
MU
CU
MU
MU
CU
CU
MU
CU
Data In
Data In
Data Out
Data Out
Notes: Single neuron can be built with mem + compute unit
Tiles are to scale out to larger, more complex algorithms

## Slide 19: Compute unit design
Taurus CUs are array based:
  Functional Units (FUs)
  Pipeline Registers (PRs)
LANE 0
LANE 1
LANE 2
STAGE 0
STAGE 1
STAGE 2
FU
PR
FU
PR
FU
FU
PR
FU
PR
FU
FU
PR
FU
PR
FU
PR
PR
PR
FU
PR
FU
PR
FU
PR
LANE 3
CU
Notes: Stages- > pipeline parallelism
Lanes -> parallel operation
- Leads to map operations
- Takeaway: lots of parallelism leads to faster execution

## Slide 20: Reduction network condenses vectors to scalars
LANE 0
LANE 1
LANE 2
STAGE 0
STAGE 1
STAGE 2
FU
PR
FU
PR
FU
FU
PR
FU
PR
FU
FU
PR
FU
PR
FU
PR
PR
PR
FU
PR
FU
PR
FU
PR
LANE 3
Notes: - Cross lane connections allows for a reduction tree

## Slide 21: Taurus: An Intelligent Data Plane
Packet
Parser
Match-Action
Tables
Map Reduce
Unit
Match-Action
Tables
Traffic
Manager
Packets In
Packets Out
Notes: - Pipeline is a collection of DSAs

## Slide 22: Example: Anomaly Detection
Packet
Parser
Match-Action
Tables
Map Reduce
Unit
Match-Action
Tables
Packets In
Packets Out
Read local features
(e.g., IP address)
Retrieve out of
network events
(e.g., failed
logins per IP)
Apply learned anomaly detection
Select a port or action
(e.g., drop if score == 1)
Send packet
to destination
Traffic
Manager
Packet
Notes: Spend more time here

## Slide 23: Evaluation: Anomaly Detection in Switches
Taurus examines every packet at every switch
Additional latency is less than port to port latency
*Overheads are calculated relative to a 300 mm2 chip with 4 reconfigurable pipelines, each drawing an estimated 25 W
Model
Lat (ns)
Area
Power
+%
+%
SVM
DNN
68
362
6.1
11.7
1.1
2.0
TP (GPkt/s)
1
1
Notes: - Simple networks not large CNNs
- Two key things: meeting line rate and area increase is minimal
- Get all this perf for little area and power

## Slide 24: Evaluation: Congestion Control at the NIC
Indigo Congestion Control LSTM Network [7]
Taurus updates every 12.5 ns (software updates every 10 ms)
*Overheads are calculated relative to a 300 mm2 chip with 4 reconfigurable pipelines, each drawing an estimated 25 W
Model
Lat (ns)
Area
Power
+%
+%
LSTM
380
23.6
4.1
TP (GPkt/s)
0.08
Notes: - Taurus data plane is also applicable to end host
- Took work that relies on CPU because of lack of NIC HW
- Show that Taurus is needed for us scale events - allows for more fast reaction
Talk: Go from ms to ns

## Slide 25: Conclusion
Introduces map and reduce to PISA
Designed to run ML inference inside a data plane
Provides orders of magnitude improvement
Taurus: An Intelligent Data Plane
Notes: Given this arch, looking forward to new ML algos
Taurus extends programmability footprint. RMT/PIFO just makes existing HW programmable. We add new forward looking functionality for ML